## Slide 1
HLS Hero Workshop
Course Workbook

## Slide 2: Table of Contents
About this Workbook | Page 3
Pre-Lab: Workshop Pre-requisites | Page 4
Lab 1: Vitis HLS Flow | Page 7
Lab 2: Vitis HLS Interfacing | Page 48
Lab 3: Vitis HLS Optimization | Page 63
Lab 4: Vitis HLS Arbitrary Precision Math | Page 79
Lab 5: Vitis HLS Vitis Libraries | Page 89

## Slide 3: About this Workbook
The contents of this workbook are created by Adiuvo Engineering & Training, Ltd.
If you have any questions about the contents, or need assistance, please contact Adam Taylor at adam@adiuvoengineering.com.

## Slide 4: Pre-Lab HLS Hero

## Slide 5: Required Hardware
Pre-Lab
None Required

## Slide 6: Downloads and Installations
Vitis 2021.2 | Download
Pre-Lab
Step 1 – Download and install the following at least 1 day prior to the workshop. This may take a significant amount of time and drive space.
Watch the video available here to show how to configure the installation

## Slide 7: Lab 1 Vitis HLS Flow

## Slide 8: What is HLS
High Level Synthesis (HLS) enables generation of RTL modules from higher level language such as C, C++, OpenCL
Of course, SW engineers still consider these low-level languages.
HLS offers several benefits for the development of Signal / Data / Image processing algorithms

## Slide 9: HLS Benefits
Developing in Higher Level language enables a faster iteration time.
Development Time decreased as untimed language – No RTL / Behavioral level
Increased level of abstraction – accelerates development
Verification time is reduced as untimed Simulation
RTL
RTL
C Design
Verified RTL
Verified RTL
Hours / Days Iteration
Seconds / Minutes Iteration

## Slide 10: Creating HLS Solutions
Software written for CPUs and software written for FPGAs is fundamentally different
Not all C constructs can be synthesised
Learn about synthesizable C/C++ coding styles.
Need to focus on correct micro architecture
  Understand the producers and consumers
  Decompose the algorithm into small section which interconnect
  Understand throughput required for each element to achieve overall performance goals
Learn how to interpret the design reports

## Slide 11: HLS Flow
Create Solution, Simulate & Debug
Synthesize
Analyse & Optimize
Package the IP
Co Simulation
Create the C Module and Test Bench – Leverage Libraries where possible
Verify algorithm performance in SW
Convert C Module to RTL
Optimize Interfaces and Performance of synthesized implementation
Simulation of the RTL module against the C Test Bench
Package for use in Vitis (XO) or Vivado (Xact IP)

## Slide 12: Untimed to Timed
Scheduling
Determines which operations occur during each clock cycle
Binding
Determines which hardware resource implements each scheduled operation
Control logic extraction
Extracts the control logic to create a finite state machine (FSM) that sequences the operations in the RTL design

## Slide 13: Clock Definition
Clock frequency & selected device used to determine timing of operations – Scheduling Phase
Uncertainty leaves time for final component placement and net routing
If left blank 27% is used

## Slide 14: Lab 1: Vitis HLS Flow
Step 1 – Open Vitis HLS 2021.2 and create a new project
Lab 1

## Slide 15: Lab 1: Vitis HLS Flow
Step 1 – Enter a project name and select a location and click next
Lab 1

## Slide 16: Lab 1: Vitis HLS Flow
Step 1 – I used the name VHlab1
Lab 1

## Slide 17: Lab 1: Vitis HLS Flow
Step 1 – Click Next
Lab 1

## Slide 18: Lab 1: Vitis HLS Flow
Step 1 – Click Next
Lab 1

## Slide 19: Lab 1: Vitis HLS Flow
Step 1 – Leave all unchanged except for part selection, click to select
Lab 1

## Slide 20: Lab 1: Vitis HLS Flow
Step 1 – Select board and select the SP701 Spartan 7 Board, Click OK
Lab 1

## Slide 21: Lab 1: Vitis HLS Flow
Step 1 – Click Finish to create the project
Lab 1

## Slide 22: Lab 1: Vitis HLS Flow
Step 1 – This will open the project ready for us to create the application
Lab 1

## Slide 23: Lab 1: Vitis HLS Flow
Step 1 – Right Click on Source and Select new Source File
Lab 1

## Slide 24: Lab 1: Vitis HLS Flow
Step 1 – Enter the name of the file as lab1.cpp, click save
Lab 1

## Slide 25: Lab 1: Vitis HLS Flow
Step 1 – Enter the code as below – or Copy from the files on the GitHub. Save the file.
Lab 1

## Slide 26: Lab 1: Vitis HLS Flow
Step 1 – Right Click on Source and Select new Source File
Lab 1

## Slide 27: Lab 1: Vitis HLS Flow
Step 1 – Enter the name of the file as lab1.h click save
Lab 1

## Slide 28: Lab 1: Vitis HLS Flow
Step 1 – Enter the code as below – or Copy from the files on the GitHub. Save the file.
Lab 1

## Slide 29: Lab 1: Vitis HLS Flow
Step 1 – Right Click on Test Bench and Select new Test Bench File.
Lab 1

## Slide 30: Lab 1: Vitis HLS Flow
Step 1 – Enter the name of the file as tb_lab1.cpp click save
Lab 1

## Slide 31: Lab 1: Vitis HLS Flow
Step 1 – Enter the code as below – or Copy from the files on the GitHub. Save the file.
Lab 1

## Slide 32: Lab 1: Vitis HLS Flow
Step 1 – From the Run menus select C Simulation
Lab 1

## Slide 33: Lab 1: Vitis HLS Flow
Step 1 – On the dialog box select the launch debugger option, click OK
Lab 1

## Slide 34: Lab 1: Vitis HLS Flow
Step 1 – This will open the debugger view, with the program paused for execution – we can run, pause, single step using the menu, along with insert breakpoints
Lab 1

## Slide 35: Lab 1: Vitis HLS Flow
Step 1 – Single Step a few of the instructions, hold the pointer over a variable and notice the contents pop up for inspection
Lab 1

## Slide 36: Lab 1: Vitis HLS Flow
Step 1 – Double click in the margin of line 29 to insert a breakpoint – this will be shown by a blue circle.
Lab 1

## Slide 37: Lab 1: Vitis HLS Flow
Step 1 – Click Run and you will see the breakpoint be hit, double click again in the margin to remove the breakpoint and hit run.
Lab 1

## Slide 38: Lab 1: Vitis HLS Flow
Step 1 – The application should run through, outputting pass or fail in the console and then terminate its run.
Lab 1

## Slide 39: Lab 1: Vitis HLS Flow
Step 1 – Exit the debug display by clicking exit debug
Lab 1

## Slide 40: Lab 1: Vitis HLS Flow
Step 1 – From the setting menu select Project Settings
Lab 1

## Slide 41: Lab 1: Vitis HLS Flow
Step 1 – Select Browse to select the top function
Lab 1

## Slide 42: Lab 1: Vitis HLS Flow
Step 1 – Select lab1 (or the name of your function if you named it differently)
Lab 1

## Slide 43: Lab 1: Vitis HLS Flow
Step 1 – Click OK
Lab 1

## Slide 44: Lab 1: Vitis HLS Flow
Step 1 – Click on run and select C Synthesis
Lab 1

## Slide 45: Lab 1: Vitis HLS Flow
Step 1 – Leave all options unchanged and select OK
Lab 1

## Slide 46: Lab 1: Vitis HLS Flow
Step 1 – Once synthesis is complete you will see the report open notice the resources and interfaces
Lab 1

## Slide 47: Lab 1: Vitis HLS Flow
Step 1 – Scroll down the report you will see the Top level Controls and Interface Info
Lab 1

## Slide 48: Lab 1: Vitis HLS Flow
Step 1 – From the Schedule menu select Schedule View
Lab 1

## Slide 49: Lab 1: Vitis HLS Flow
Step 1 – Examine the schedule view
Lab 1

## Slide 50: Lab 1: Vitis HLS Flow
Step 1 – From the run menu select Co-Simulation
Lab 1

## Slide 51: Lab 1: Vitis HLS Flow
Step 1 – Leave the options unchanged and click OK
Lab 1

## Slide 52: Lab 1: Vitis HLS Flow
Step 1 – Observe the report which shows the completion of the Co Simulation and pass / fail.
Lab 1

## Slide 53: Lab 1 Summary
Lab 1 Summary
The concludes lab 1, throughout this lab we have demonstrated
How to create a project in Vitis HLS
How to create source and test benches
How to run C simulation
How to set up the project for synthesis
How to synthesize the design
How to run Co-Simulaiton

## Slide 54: Lab 2 Vitis HLS Interfacing

## Slide 55: Interfacing
Interfacing depends on flow
Vitis - XO
  AXI – Data Accessed via Memory Map
  AXIS – Data Accessed via Stream
  AXI Lite – Register Access
Vivado – IP XACT
  Block Level – Controls Flow / Status
  Protocol Level – Controls

## Slide 56: Vivado Interfacing
Instantiate appropriate interface to integrate with design
Do we want to start and stop block, synchronize or be data driven.
Are we controlling the block from SW
What about data interfaces.

## Slide 57: Lab 2: Vitis HLS Interfacing
Step 1 – Create a new project called VHLab2, click OK.
Lab 2

## Slide 58: Lab 2: Vitis HLS Interfacing
Step 1 – Create a new source file called lab2.cpp and enter the code below or copy from the GitHub.
Lab 2

## Slide 59: Lab 2: Vitis HLS Interfacing
Step 1 – Create a new source file called lab2.h and enter the code below or copy from the GitHub.
Lab 2

## Slide 60: Lab 2: Vitis HLS Interfacing
Step 1 – Create a new source file called tb_lab2.cpp and enter the code below or copy from the GitHub.
Lab 2

## Slide 61: Lab 2: Vitis HLS Interfacing
Step 1 – Run a C Simulation in the debugger, notice how this time the application is batch based
Lab 2

## Slide 62: Lab 2: Vitis HLS Interfacing
Step 1 – Close the C Simulation and open the Lab2.cpp file, select the directives' view. Right click on the lb2_label0 and select Insert Directive.
Lab 2

## Slide 63: Lab 2: Vitis HLS Interfacing
Step 1 – Insert the directive LOOP_TRIPCOUNT this informs the tool how many times the loop will execute in the maximum case.
Lab 2

## Slide 64: Lab 2: Vitis HLS Interfacing
Step 1 – Run the Synthesis you will notice the Trip Count is now recorded under the lab2 label0
Lab 2

## Slide 65: Lab 2: Vitis HLS Interfacing
Step 1 – Examine the HW Interfaces and notice the RAM Interfaces are AP_MEMORY and Register Interfaces.
Lab 2

## Slide 66: Lab 2: Vitis HLS Interfacing
Step 1 – In the synthesis view add in a new directive for the source code for the port loop. Select INTERFACE directive and for the mode select S_AXILITE
Lab 2

## Slide 67: Lab 2: Vitis HLS Interfacing
Step 1 – In the synthesis view add in a new directive for the source code for the function. Select INTERFACE directive and for the mode select S_AXILITE
Lab 2

## Slide 68: Lab 2: Vitis HLS Interfacing
Step 1 – The Directives should appear as shown in the directives tab – Rerun synthesis
Lab 2

## Slide 69: Lab 2: Vitis HLS Interfacing
Step 1 – Examine the HW Interfaces in the report and notice control of the block and loop register are now AXI registers
Lab 2

## Slide 70: Lab 2 Summary
Lab 2 Summary
The concludes lab 2, throughout this lab we have demonstrated
How to inform the synthesis tool about number of loop iterations
How to control register interfaces to use AXI Interfaces
How to control the IP Block control signals be Implemented as AXI

## Slide 71: Lab 3 Vitis HLS Optimization

## Slide 72: Lab 3: Vitis HLS Optimization
Step 1 – Create a new project called VHlab3.cpp
Lab 3

## Slide 73: Lab 3: Vitis HLS Optimization
Step 1 – Create a new source file called lab3.cpp and enter the code below or copy from the GitHub.
Lab 3

## Slide 74: Lab 3: Vitis HLS Optimization
Step 1 – Create a new source file called lab3.h and enter the code below or copy from the GitHub.
Lab 3

## Slide 75: Lab 3: Vitis HLS Optimization
Step 1 – Create a new source file called tb_lab3.cpp and enter the code below or copy from the GitHub.
Lab 3

## Slide 76: Lab 3: Vitis HLS Optimization
Step 1 – Right Click on Test Bench File and select add Test Bench File
Lab 3

## Slide 77: Lab 3: Vitis HLS Optimization
Step 1 – Add in the input.dat file provided on the GitHub
Lab 3

## Slide 78: Lab 3: Vitis HLS Optimization
Step 1 – Run the C Simulation and ensure the result is as shown below.
Lab 3

## Slide 79: Lab 3: Vitis HLS Optimization
Step 1 – Select the top function of Sensor_Filter to allow synthesis – perform synthesis.
Lab 3

## Slide 80: Lab 3: Vitis HLS Optimization
Step 1 – Observe the synthesis interval and resources reported in the synthesis report.
Lab 3

## Slide 81: Lab 3: Vitis HLS Optimization
Step 1 – Open the Function Call Graph for the Synthesis.
Lab 3

## Slide 82: Lab 3: Vitis HLS Optimization
Step 1 – Observe the information presented, change the heat map.
Lab 3

## Slide 83: Lab 3: Vitis HLS Optimization
Step 1 – In the directives view for the source code add in a pragma to unroll the loop labelled accum.
Lab 3

## Slide 84: Lab 3: Vitis HLS Optimization
Step 1 – In the directives view for the source code add in a pragma to partition the array Input .
Lab 3

## Slide 85: Lab 3: Vitis HLS Optimization
Step 1 – Rerun synthesis and observe the interval and resources again.
Lab 3

## Slide 86: Lab 3 Summary
Lab 3 Summary
The concludes lab 3, throughout this lab we have demonstrated
How to add optimization pragmas
How optimization pragma will change the resource and latency performance
How to visualize the optimization impacts

## Slide 87: Lab 4 Vitis HLS Arbitrary Precision Math

## Slide 88: Lab 4: Vitis HLS Arbitrary Precision Math
Step 1 – Create a new project called vhlab4.
Lab 4

## Slide 89: Lab 4: Vitis HLS Arbitrary Precision Math
Step 1 – Create a new source file called lab4.cpp and enter the code below or copy from the GitHub.
Lab 4

## Slide 90: Lab 4: Vitis HLS Arbitrary Precision Math
Step 1 – Create a new source file called lab4.h and enter the code below or copy from the GitHub.
Lab 4

## Slide 91: Lab 4: Vitis HLS Arbitrary Precision Math
Step 1 – Create a new source file called tb_lab4.cpp and enter the code below or copy from the GitHub.
Lab 4

## Slide 92: Lab 4: Vitis HLS Arbitrary Precision Math
Step 1 – Run the Synthesis observe the interval and the resources required.
Lab 4

## Slide 93: Lab 4: Vitis HLS Arbitrary Precision Math
Step 1 – Examine the analysis view to see the operations involved.
Lab 4

## Slide 94: Lab 4: Vitis HLS Arbitrary Precision Math
Step 1 – In the file lab4.h comment out the line define float_type.
Lab 4

## Slide 95: Lab 4: Vitis HLS Arbitrary Precision Math
Step 1 – Rerun synthesis and observe the interval and resources.
Lab 4

## Slide 96: Lab 4 Summary
Lab 4 Summary
The concludes lab 4, throughout this lab we have demonstrated
How to switch between floating point and arbitrary precision in your application
The benefit of using arbitrary precision numbers
The difference in performance between the use of floating-point vs arbitrary precision

## Slide 97: Lab 5 Vitis HLS Vitis Libraries

## Slide 98: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Open the Vitis libraries repository in GitHub.
Lab 5

## Slide 99: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Download or clone the repository.
Lab 5

## Slide 100: Lab 5: Vitis HLS Vitis Libraries
Step 1 – If you downloaded the Zip Extract the files .
Lab 5

## Slide 101: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Create a project called vhlab5.
Lab 5

## Slide 102: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Right click on source and select Add Source File .
Lab 5

## Slide 103: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Select the files, data_path.hpp, top_module.cpp and top_module.hpp from the location
<install>\Vitis_Libraries\dsp\L1\examples\1Dfix_impluse\src
Lab 5

## Slide 104: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Right click on Test Bench and select Add Source File .
Lab 5

## Slide 105: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Select the file main.cpp from the location
<install>\Vitis_Libraries\dsp\L1\examples\1Dfix_impluse\src
Lab 5

## Slide 106: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Select the fft_top as the top function for the project
Lab 5

## Slide 107: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Set the Cflags and Csimflags to
-I../../../../../GIT/Vitis_Libraries/dsp/L1/include/hw/vitis_fft/fixed
Lab 5

## Slide 108: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Run synthesis this might take some time
Lab 5

## Slide 109: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Examine the function call graph
Lab 5

## Slide 110: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Examine the Dataflow graph
Lab 5

## Slide 111: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Notice there is a timing error,
Lab 5

## Slide 112: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Right click on the error and select go to timing violation
Lab 5

## Slide 113: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Observe the timing violation in the schedule viewer
Lab 5

## Slide 114: Lab 5: Vitis HLS Vitis Libraries
Step 1 – Back in the timing violation, go to the source- notice the line of code causing the delay is highlighted.
Lab 5

## Slide 115: Lab 5 Summary
Lab 5 Summary
The concludes lab 5, throughout this lab we have demonstrated
How to access Vitis Libraries
How to include Level One elements from the library within Vitis HLS
How to include the Vitis libraries to build to application
How to observe the results in the function call and dataflow graph
How to identify a timing violation
How to view the violation in the schedule viewer
How to identify the violation in the source code.